## Slide 1: Energy Conservation Building Code (ECBC)
An Overview
(please switch on speakers for audio explanation)

## Slide 2
Presented by:
Dr.-Ing. Jyotirmay Mathur
Acknowledgements:
Dr. Vishal Garg, Dr. Satish Kumar, Prof. Rajan Rawal, Ms. Surekha Tetali,

## Slide 3: ECBC: Why Comply
ECBC
Energy Savings for project
Legal Requirements
Long Term Benefits

## Slide 4: ECBC: Key Features
Sets minimum energy efficiency standards for design and construction
Encourages energy efficient design or retrofit of buildings
Ensures that the building design does not constrain the building function, comfort, health, or the productivity of the occupants
Has appropriate regard for economic considerations

## Slide 5: Application of ECBC
Buildings with 100kW load or 120kVA
contract demand
Buildings having 1000m2 conditioned
floor area (recommended)
New construction and major renovation
Caveat: National Building Code 2005 is the reference document/Standard where the code is found in conflict with safety, health or environmental codes

## Slide 6: Application of ECBC
ECBC is:
Currently optional
To be made mandatory in future
Already mandatory in few States

## Slide 7: ECBC: Types of Building Covered
ECBC applies to any building that is not in the
residential, agricultural, and industrial sector.
Office buildings (IT parks)
Government buildings
Hospitals
Retail malls
Hotels

## Slide 8: ECBC Exemptions
Buildings not using electricity or fossil fuels
Building portions that use energy primarily for manufacturing process
Multi-family buildings of three or fewer stories above grade, and single-family buildings
Following buildings types are exempted from adherence to ECBC:

## Slide 9: Alterations covered under ECBC
Addition to existing buildings:
Where the [addition + existing building] exceeds the conditions of eligibility
Addition and new equipment has to comply with code

## Slide 10: ECBC: Alterations Included
ECBC is applicable to these alterations:
Alterations in equipment/control device of HVAC system
Alteration to service hot water system
Alteration to lighting
Alterations to electric power systems and motors
Alteration to lighting: ECBC adherence is exempted if replacement is < 50% luminaries provided alterations do not increase lighting load

## Slide 11: ECBC: Alterations Excluded
ECBC is not applicable to these alterations:
Replacement of glass in existing sash or frame
Modification to roof/ceiling/walls
(U-factor, SHGC equal or lower than existing glazing)

## Slide 12: ECBC: Climate Zone Specific Application
ECBC suggests different compliance standards for these climate zones:
Hot – Dry
Warm – Humid
Composite
Temperate
Cold

## Slide 13: ECBC: Provisions
ECBC provisions apply to:
Building envelope
Mechanical systems and equipment
Service hot water heating
Interior and exterior lighting
Electrical power and motors

## Slide 14: ECBC: Routes of Compliance
Routes/Types/Areas of Compliance | Description
Component-based (prescriptive) | Requires little energy expertise; provides minimum performance requirements; no flexibility
System-based (Prescriptive with trade-off) | Allows some flexibility through the balance of some high performance components with other lower performance components
Whole building design analysis (performance): | Allows flexibility in meeting or exceeding energy efficiency requirements (as compared to a baseline building)

## Slide 15: ECBC: Modes of Compliance
Approaches | Mandatory Provisions for ECBC | Flexibility | Expert Knowledge | Linear Approach | Use of Energy Simulation
Prescriptive | Required | Low | Low | Yes | No
Prescriptive with Trade-off | Required | Medium | Medium | No | Yes
Performance based | Required | High | High | No | Yes

## Slide 16: ECBC: Prescriptive Methods
All building components need to comply the code individually. This is likely to increase the initial cost of buildings. However, in the long run energy consumption would reduce and result in net saving. For envelope, trade off is permitted.

## Slide 17: ECBC: Trade-off Method
Calculate envelope performance factor of building using prescriptive values and formulae below:
Calculate EPFroof, EPFwall, EPFfenest using factors given in ECBC as per the climatic zone, orientation, and geometry
Calculate the EPF with relaxed U-value if you find it difficult/costly to meet one specification. Example: U-value of wall
Improve some other part such as roof, window beyond the prescriptive requirement of ECBC, so that the final EPF is not more than the EPF by all prescriptive values.
The new EPF would be higher compared to the previous value if the specification is inferior to prescriptive value.

## Slide 18: ECBC: Simulation Method
Requires energy simulation of proposed building
Needs to ensure that energy consumption of building does not exceed specified limits for similar buildings
Allows use of any combination of specifications related to envelope and equipment
Accepts only hourly simulation
Simulation method:

## Slide 19: ECBC: Major implications
Requires higher cost of envelope
Requires costlier lighting fixtures and controls

## Slide 20: ECBC: Major implications
Reduces energy consumption
Reduces peak demand/contract demand
Saves through reduced size of transformer, DG back up, wiring etc.
Reduces upfront expenses for HVAC equipment

## Slide 21: ECBC: Macro Level Benefits
Reduces load on utility
Flattens load profile
Ensures Effective load management
Ensures grid stability due to less fluctuations in demand
Reduces breakdowns/power-cuts
Reduces installed capacity requirements

## Slide 22
Thank You